## Slide 1
LAKE MAP · DUPLICATE CONSTELLATION · TILT DISAMBIGUATION
Two constellations the matcher cannot tell apart
Identical to within the matcher's 0.5 m inlier tolerance — but standing on different ground.
CONSTELLATION GEOMETRY
Pairwise side | Group A | Group B | Δ
short A1–A3 / B2–B3 | 10.587 m | 11.084 m | 0.496
medium A2–A3 / B1–B3 | 14.600 m | 14.863 m | 0.262
long A1–A2 / B1–B2 | 23.824 m | 24.303 m | 0.479
centroid separation | — | — | 59.36 m
matcher inliers | 3 / 3 | 3 / 3 | tied
Max vertex mismatch 0.496 m — inside the 0.500 m inlier tolerance. Shape alone cannot choose.
MEASURED vs DTM-PREDICTED ATTITUDE
Robot at / hypothesis | Roll | Pitch | Resid. | Verdict
SITE A measured | +0.15° | +2.47° | — | 
hypothesis A | +0.18° | +2.19° | 0.28° | consistent
hypothesis B | −7.17° | −2.62° | 8.91° | eliminated
SITE B measured | −8.22° | −2.87° | — | 
hypothesis A | +0.18° | +2.19° | 9.81° | eliminated
hypothesis B | −7.17° | −2.62° | 1.09° | consistent
Predictor's own error over 11 known-good poses: mean 0.253°, max 0.435°.
RESULT
The wrong hypothesis misses by 8.9–9.8°, the correct one by 0.3–1.1° — a 9–12× gap, in both directions.
Lake Gazebo world, single local machine. Attitude from /compass/data; terrain from lake_dtm.npy; landmarks from lake_objects.yaml. No simulator ground truth used for pose. Constellation matcher unmodified — it still separates these by a 15 m prior check, not by tilt.